## Slide 1: Hardware Loop Support
COMP4211 Advanced Architectures
Project by Shannon Koh

## Slide 2: Motivation
No explicit loop support in general-purpose processors
  Diversity of loop implementations
    Thus, ASIPs have ZOL support
  Different hardware and software approaches to optimise loop execution
Common programming paradigms (general purpose) also execute many standard “for” loops
  Try to exploit this!

## Slide 3: Goals
Reduce branch misprediction penalties
  Try to precompute branch decisions
Reduce hardware complexity
  Remove complex predictors
Reduce software complexity
  Loop instructions reduce code size
  No loop unrolling
Reduce loop management overhead
  Manage loop in parallel to execution

## Slide 4: Loop Analysis
for (i = 0; i < N; i++)
{
x = x + i;
y = y + x;
}
0000: addi R1, R0, #0
0001: addi R6, R0, #(N-1)
0002: addi R2, R2, R1
0003: addi R3, R3, R2
0004: addi R1, R1, #1
0005: bne R1, R6, #-4
0000: addi R1, R0, #0
0001: addi R6, R0, #(N-1)
0002: loopinc R1, R6, #1
0003: addi R2, R2, R1
0004: addi R3, R3, R2

## Slide 5: Loop Management
Loop Management Variables:
  CounterReg: R1
  TargetReg: R6
  StartAddress: 0003 (next PC)
  EndAddress: 0004 (relative)
0000: addi R1, R0, #0
0001: addi R6, R0, #(N-1)
0002: loopinc R1, R6, #1
0003: addi R2, R2, R1
0004: addi R3, R3, R2

## Slide 6: Loop Execution
When PCNEXT == EndAddress, increment and check
Compare and Branch
  If EndAddress is reached and R1 != R6 then update PC with StartAddress
0000: addi R1, R0, #0
0001: addi R6, R0, #(N-1)
0002: initinc R1, R6, #1
0003: addi R2, R2, R1
0004: addi R3, R3, R2

## Slide 7: Performance
Source: Application of ZOL and AGEN in General Purpose Computing
Jinyung Namkoong, EE 482A Project, Spring 2000
N: Number of instructions
W: Instruction issue width
P: Miss rate for prediction
δ: Instructions removed by ZOL
X: Branch miss penalty
BBsize: Basic Block Size

## Slide 8: Coverage
Source: Application of ZOL and AGEN in General Purpose Computing
Jinyung Namkoong, EE 482A Project, Spring 2000
ZOLs not handled at the compiler level
Only regular branch distances were considered

## Slide 9: Implementation
Advanced support with loop nest stacks
Compiler support required
Looping of non-ZOL type loops possible
Test Behavioural VHDL Implementation
  Standard MIPS processor
    97848 cells, 55 MHz
    No register file and memory
  Loop Unit
    3086 cells, 190 MHz
    Unoptimised

## Slide 10: Conclusion
Viable alternative
Provisions
  Compiler support
Future work
  Compiler requirements
  Actual benchmark code testing